## Slide 1: COMP6236
Lab 1

## Slide 2: A reminder of memory layout

## Slide 3: A reminder of interesting registers
Caller saved: %eax, %ecx, %edx
  You must save these before a function call if you need them
Callee saved: %ebx, %edi, %esi
  You must save these before any work if you need them
Base pointer: %ebp
  Points to the “bottom” of a stack frame
Stack pointer: %esp
  Points to the “top” of a stack frame
Instruction pointer: %eip
  Generally don’t need to worry about this one

## Slide 4: A reminder of interesting registers
EAX,EBX,ECX,EDX - "general purpose", more or less interchangeable
EIP – INSTRUCTION POINTER – The next instruction to be executed
EBP – FRAME POINTER - used to access data on stack - when this register is used to specify an address, SS is used implicitly
ESI,EDI - index registers
ESP – STACK POINTER

## Slide 5: What happens when you call a function
You push the parameters onto the stack
You leave behind the return address
You jump to the next function
You now have a new stack frame
  EBP = ESP

## Slide 6: Today’s Lab
Taking a look at C
Taking a look at debugging
Having a go at reverse enginerring
Having a go at a buffer overflow

## Slide 7: Task 1
Log in as user task1, password unicorn
Take a look in /home/task1
Take a look at the source code in test.c
What does the program do?
Now have a go at debugging it with gdb
  gdb test

## Slide 8: Task 1 – Part 2
Part 1 is easy
  There are debugging symbols
  Can see the source code and what is going on
  Can examine variables, functions
Now have a go at debugging test2
  No debugging information!
  Can you see how it differs to the first test?
  The difference is your key to Task 2!

## Slide 9: Task 2
Log in as user task 2 with the password you got from task 1
The task is in /home/task2
This time, you have no source code or debugging information
You just have to use gdb
Use gdb to step through the program and examine how it works and find the correct name
The correct name is the password to task 3

## Slide 10: Task 3
This is where it gets exciting!
Log in as task3 with the password you got from task 2
In /home/task3 there is an elevate program
This is a simple version of ‘sudo’
It gives you root… if you know the password

## Slide 11: Task 3
We notice that the application is vulnerable to a buffer overflow
If we put in a longer password than we should, we get an error – something is going wrong here!
What we need to work out is how to be able to get the application to execute the part that gives us root
We can’t debug the elevate application itself – Linux won’t let us, so we need to make a copy and experiment, learn how to break it, then put it to use

## Slide 12: Task 3
By examining the application, we can work out where the function is that performs the elevation
We need to construct an input that uses buffer overflow in the password input that lets us break into this part of the application
Once we’ve worked out how to do it on our test version, we can do it on the real version… and get root!

## Slide 13: Using GDB
Always start with the following two commands:
  set disassembly-flavor intel
  set disassemble-next-line on
This will let us see what is going on at each stage in assembly

## Slide 14: Using GDB
layout src
  Shows the source code (if you have it)
layout asm
  Shows the assembly (next best thing)
layout registers
  Shows what all the registers are doing!

## Slide 15: Using GDB
When we have debugging symbols available
  Next and step lets us move to the next line of code, or step into the next line of code
When we don’t, we have to work with the assembly
  ni = next instruction
  si = step instruction

## Slide 16: Using GDB
We can print out something using p
  p/<format> <value> will print out the value
We examine a memory address using x
  x/<format> <address> will display what is in that memory address
Formats you might want to use
  s = string
  i = instruction
Keep pressing enter to see more

## Slide 17: Using GDB
Use info
Info file
  Shows the entry point!
Info frame
Info registers
Info locals

## Slide 18: Using gdb
Break *<address>
Break <name>
Sets a breakpoint – stop when the code reaches there!

## Slide 19: Using GDB
Use run to run with input
run < <(python -c 'print "a"*28 + “b”*16')

## Slide 20: Using GDP
See what’s going on
Info registers
  What’s in the registers
x/5i $eip
  Show the next 5 instructions
Etc.

## Slide 21: Getting the Virtual Machine
http://go.ssago.org/6236
Download the Virtual Machine
Put it on the X: Drive
Open Virtual Box
Import the Virtual Machine
Run it
SSH to 192.168.56.101
Log in as task1:unicorn